# Chapter 1: Infrared Control Robot

insert image 1.1 – IR_robot.jpg
## Introduction
  In this chapter, we will use a standard motorized platform (MakeBlock kit) in conjunction with an Arduino, Infrared receiver, motor-controller shield, and Infrared Remote to build a remote controlled robot. At the end of this chapter, you should understand the concepts behind infrared data transmission, serial binary data transfer, Arduino data String objects, and reading pulse signals with an Arduino. Now on to the fun stuff.
  The purpose of this chapter is to create a wireless robot controller link for as cheap as possible. As I mentioned, this book is meant to focus on the manipulation of code to achieve the desired results instead of building hardware around a problem (thanks Harald!), so we will be using our standard robot-base kit, motor-controller, battery, and Arduino to get started. This chapter will not discuss how to connect your Arduino to your robot-base, but rather how to connect the sensors from this chapter to your Arduino.

insert image 1.2 – parts_required.png

  You will need very few things to test the code in this chapter – an infrared detector from Radio Shack, an infrared emitter (TV remote or IR helicopter remote), your Arduino, and a computer. The infrared detector module from Radio Shack is easy to directly connect to the Arduino and only costs about $4.00. For testing purposes, you can use nearly any infrared remote from any TV, VCR, DVD, or other appliance. If you must purchase one, most electronics stores have a cheap IR remote for under $10. Alternatively, I will also show you how to use a recycled IR toy helicopter remote that has 3 joystick channels and 2 buttons – these are easily obtainable and provide more real-time control of your robot.

### Parts List: Infrared Controlled Robot
Image	Part Name	Retailer	Price
	Infrared receiver module	Radio Shack (276-640), Sparkfun.com (SEN-10266)	$2 - $4
	3-channel Infrared Helicopter Remote Control	Radio Shack, Sparkfun, or just find one	$5
	Robot base – Makeblock 2WD kit with Arduino Uno and Motor-shield (Arduino and motor-shield sold separately)	Seeed Studios	$69

  While the Arduino code for this project has a few different parts that we will discuss, the overall objective is to get a stream of data, and ultimately a specific code from the infrared detector for each function on our infrared remote control. To do this, we will need to connect the infrared detector to our Arduino so we can read the signals and evaluate them. Then we will need to record the data that is received for several buttons on our remote control. Once we record the codes that are being sent across from the remote, we can assign some actions for our robot to carry out when called. While most IR remote controls have different codes, you can decode as few buttons as you like to get your robot moving. 3 or 4 functions should be sufficient for basic movement (up/down/left/right). First, we will discuss how an infrared detector works.
## The Infrared Detector
  An infrared detector is simply a transistor switch that is opened when a sufficient amount of infrared light enters the detector (which also acts as the base pin of this transistor). You can use a standard infrared detector LED to read infrared light levels and they work well for things like line-following robots and short-range object detection, but they have some shortcomings when dealing with reliable data transfer. They typically have 2 pins, an emitter and collector, that function as a normal transistor, but the base pin replaced by the LED detector, which is used to switch the transistor. Below is a standard infrared detector and emitter pair from Radio Shack (#276-142):

insert image 1.3 – infrared_leds.jpg

  While basic infrared detectors have their place, there are a number of factors that can cause interference, usually from various other light sources. If this happens, the signal will be distorted and therefore useless to decode. Luckily, there is an inexpensive solution to this problem.
  To avoid signal noise and interference, most infrared control devices are tuned to a specific frequency when they transmit signals (similar to a Serial data transfer speed - eg. 9600bps) so that the receiving transistor knows to only listen to infrared signals that are transmitted at that same frequency (usually 38kHz). This means that you can buy a special infrared detector module that has a logic chip built-in to ignore non-control related infrared light. The image below shows a typical IR receiver module:

insert image 1.4 – ir_labeled.png

  These detectors can be found in nearly any VCR, DVD player, TV, or other remotely controlled indoor appliance - and can easily be read using your Arduino. Radio Shack also sells Infrared Receiver Modules for about $4 each (part #276-640) while Sparkfun sells them for only $2 each (SEN-10266), and both can be directly connected to the Arduino. The receiver contains 3 pins: +5v, GND, and Input. Simply connect these pins to your Arduino, and you can read the input of the IR module from any Arduino I/O pin.
  How do you read the sensor? Alright, alright, let's get to it.
## Reading Infrared signals
  Infrared data transmission is shockingly simple to implement and equally as cheap. To send a signal using infrared light, you will need two devices: an infrared emitter and an infrared detector. The emitter is nothing more than an LED that only emits light in a specific wavelength (the infrared wavelength is 750 nm - 1 mm) - though these LED's are powered the same way as a normal LED, the light that is emitted is undetectable to the human eye (that is, you can't see it) and must be viewed using a digital camera or other filtering device. The infrared detector is actually a transistor switch that uses infrared light to activate its Base pin, instead of electrical current or voltage. The standard IR detector has 3 pins – power, ground, and signal. By applying +5v and Gnd signals to the power pins, we can simply plug the signal pin into any digital input pin on the Arduino (so any pin).
  As you may recall, a transistor is a solid-state electrical switch that can be turned On and Off thousands of times every second. The high speed at which the infrared detector can read infrared signals is ideal for low bandwidth data transfer using a string of binary data (0's and 1's) bits. To put it more simply, the typical infrared emitter device (remote control for your TV) sends out about 20 or so timed electrical pulses, which are meant to be read in order as a specific control code, each time you press a button. Each pulse that is emitted is one of two lengths - if intended to be interpreted as a LOW bit (0), the pulse duration is approximately 500 microseconds (0.5mS), whereas the duration of a pulse that is intended to be interpreted as a HIGH bit (1) is approximately 1100 microseconds (1.1mS). We can easily read each pulses that is transmitted using the pulseIn() command on the Arduino as shown in code example 1.1:

Code example 1.1 – reading a pulse
  int pulse_pin = 6; // create a variable called pulse_pin attached to pin D6 on Arduino
  pulse_val = pulseIn(pulse_pin, HIGH, 20000); // read the pulse_pin on D6, to see if a pulse is present

  The pulseIn(pin, state, timeout) command takes 3 arguments and will watch a given pin (the first argument - D4 in the example above) as an input. When the pin changes state from 0v to +5v, this pulseIn() command will start recording the time duration in microseconds of how long that pin stays HIGH, which is the second argument that determines what state of the pulse to measure (LOW or HIGH). Once the electrical pulse is complete and the voltage level drops back down to 0v, the time value that was calculated is then passed into the "pulse_val" variable shown above. The third argument is optional, but determines how long (in microseconds) the Arduino will wait on that pin to receive a pulse before it continues to the rest of the loop - if omitted, the default "timeout" value is 1 second (100000uS).
  So now we know how to read the individual pulses that come out of the infrared detector, but those values are intended to be converted into binary or boolean data (1's or 0's) – where 1 corresponds to a HIGH signal and 0 corresponds to a LOW signal. For this we must write a simple function to convert the timed values into boolean values.
## Booleanize
  The IR receiver module will convert infrared light received into a pulse of electricity that is either 500mS in duration or 1100mS (give or take a few microseconds), depending on the intended bit. So I decided to use 750uS as the threshold value that is roughly between 500uS and 1100uS – any pulse duration below the threshold value will be converted to a “0” and any pulse above the threshold will be converted to a “1”. Since a binary bit value type is called a "boolean", I named the function to convert these values "booleanize", see code example 1.2:

Code example 1.2 – converting pulse time values into boolean values (0 or 1)
    void booleanize(){
      if (pulse_val > 750){
        pulse_val = 1;
      }
      else {
        pulse_val = 0;
      }
    }

  Well then... that was easy, right? We know that a boolean value can only be either 1 or 0, and we knew that the observed pulse length was either 500mS or 1100mS, so I just picked a value near the middle (750mS) to see if the pulse_val was above or below that and then assigned a 1 or 0 to the value accordingly. Congratulations, you've just been booleanized.
  Now that we have a clean data bit from each pulse, we need to add the booleanized pulses from each signal into one variable that can be analyzed – enter the String object.
## Arduino String object
  Typically when using the Arduino, you will see the integer data type (ie. int x = 3;) used to initiate variables for pin assignment, holding non-floating point numbers, or even variable names. We also discussed boolean variables that contain a binary piece of data which can only be either True or False (1 or 0 respectively). The easiest way to create a piece of data that contains the code we need from the IR remote is to create what is called a “String” object that can contain multiple characters in a row, and have more added to the end as needed. A simple string can be created by declaring the String variable type (note the capital S in String), assigning a name to the variable, then assigning a value by placing any characters between quotation marks like so:

String test_string = “Hello”

  Notice that this string contains characters like “H” and “e”. You can also place digits in a string, though they will not be interpreted as integers that can be added/subtracted/etc.., they will only be recognized as the character representation of a digit, such as the string “// create a variable called pulse_pin attached to pin D6 on Arduino3”. Where the digits 3 + 8 would equal 11, the strings “3” + “8” would equal “38”. We will discuss more about adding strings, but first let us discuss the positioning of characters in a string.
### String Index
  Each character in the string is indexed by its position, which because of a programming technique called zero-based numbering or zero-indexing, the very first character in the string holds an index of 0 rather than 1, as you might normally think. This means that in the string “Hello”, the character at index 0 would be “H” and the last character in the string “o” would hold an index of 4. Keep this in mind as we will be accessing parts of the string by their array indexes, and this can be a source of confusion. The string index also allows us to look up the value of a given index, once we have a string. This is how we will check the strings to see if they contain the codes we are looking for. Furthermore, we can even check multiple index values at the same time using an Arduino String method called substring.
### Substring matching
  The Arduino language has a method called “substring()” that we can use on String objects that will allow us to check a specific index (or range of indexes) to see if they match another string. We will use this feature after recording the values from the IR remote output and storing them in the Arduino code – then when we are using our robot, we can compare the currently received code from the IR remote against the ones we recorded to determine the desired function from our robot.
  What? Well, let me put it this way. If you have a sample string with 4 characters “0001”, and we wanted to check and see if the character at index position 3 (the one at the end) is equal to “1”, we would use the substring method to make this query, as in example 1.3:

Code example 1.3 – evaluating a single substring index
  String tester = “0101”
  if (tester.substring(3) == "1"){
    // do something cool here
  }

  You would definitely get to do something cool there, because that if statement would pass since the last character (index 3) in the string above named tester is equal to 1. By rearranging the 0's and 1's into different orders, you can see that there are quite a few combinations of unique binary codes that we could interpret. For example, using a 4 digit binary code, we can derive 16 unique values (not listed in any particular order):
0000, 0001, 0010, 0011, 0111, 0110, 0101, 0100, 1000, 1001, 1010, 1011, 1100, 1101, 1110, 1111.
  This means that we can use a single 4-character binary string to represent 16 different functions on our robot... now keep in mind that the string we will be building contains closer to 20 characters. That's over 1,000,000 combinations of individual codes (2^20) - luckily there are only a handful of functions that we will use for our robot, so we don't need to decode all 1 million of the possible codes.
  Similar to the example above, we can also match a range of index values to check against another string, by passing two numbers into the substring() command, as shown in example 1.4:

Code example 1.4 – evaluating a range of range of substring indexes
  String tester = “0101”
  if (tester.substring(0,3) == "010"){
    // do something cool here
  }

  The above substring evaluation would also return true because the index values from index position 0 up to (but not including) position 3 are equal to “010”. It is slightly confusing that the second number entered into the substring() method is not the index of the last value that will be evaluated, but the index position after. Keep this in mind when using this method.
  So the next question then is how to get each of the boolean values obtained by the Arduino into the string object that we create? By using a thing called string concatenation, which simply means adding each new value to the end of the existing string... let's talk more about that.
### String Concatenation
  One interesting feature about strings (that we will use) is that you can append or concatenate one string onto the end of another, without disrupting the position of the original characters, as shown in example 1.5:

Code example 1.5 – concatenating (combining) two strings together
  String stringOne = “Hello ”;
  String stringTwo = “World”;
  String stringThree = stringOne + stringTwo;
  stringThree => “Hello World”

  Notice how we declared 3 separate string objects, the third one being the sum of the first two. We can simply add stringOne and stringTwo together, which appended the content of stringTwo to the end of stringOne. The final line is what the resulting stringThree would return.
  We will similarly use string concatenation to keep adding each boolean value that we decode from the IR detector, and arrange them in the order that they were received. This way we can observe a consistent binary string which will vary depend on what function is being called from the remote.
  In our code, it will look slightly different because we will programatically be adding the new values being read into the existing string, instead of doing it manually as in the example above. Now if we add the “booleanize()” and “pulseIn()” functions that we discussed earlier in the chapter, along with a string concatenation loop to add all the values into the string, we can start to see how the string is formed in example 1.6:

Code example 1.6 – Reading IR signals from a remote on your Arduino
// Basic Infrared receiver test - Upload code to Arduino
// Connect IR detector/receiver module Radio Shack (#276-640) to pin D12 (also power/gnd pins)
// Open Serial Monitor on Arduino IDE, set speed to 9600 baud
// Point Infrared remote (TV/VCR/DVD/IR Helicopter, etc..) and push a button
// See values on monitor - should look somthing like "00000010101000000010" +/- a few digits

int pulse_pin = 12; // connect IR receiver to this pin- I used pin D12, but any pin will work.
int pulse_val = 0; // create a variable to store the pulse values from the IR detector
boolean reading = false; // a boolean variable to check if the IR sensor is still receiving a string
String IRstring = ""; // initiate an empty String object to hold all of the booleanized pulse values

void setup() {
  Serial.begin(9600); // start serial monitor at 9600 bits per second
  pinMode(pulse_pin, INPUT); // input pulse signal from infrared remote
}
void loop() {
   pulse_val = pulseIn(pulse_pin, HIGH, 10000); // get a pulse reading from the IR sensor
  // now check to see if it is any pulse was read from the sensor
  if (pulse_val > 0){
    reading = true; // assert that we are reading a signal
    if (pulse_val > 750){pulse_val = 1;} // booleanize to 1 if above 750uS (closer to 1100uS)
    else {pulse_val = 0;} // booleanize to 0 if below 750uS (closer to 500uS)
    IRstring = IRstring + pulse_val; // append each new value to the string data object
  }
  else {
    // if this is the first 0 reading after a string, finish that string and print the value
    if (reading == true){
      Serial.println(IRstring); // Print the full String
      IRstring = ""; // reset the string object to be empty "", so we can read the next one
    }
    reading = false; // no longer reading a pulse, set reading boolean to false and wait for a pulse
  }
}

If everything is working correctly, you should be pushing buttons on your remote and seeing strings of data on your Serial monitor similar to the image below:
insert image 1.5 – infrared_serial_monitor_test.png

  Great, so now you are getting string after string after string and you are probably wondering what you are going to do with all of these strings. Turns out, we are going to pick a few and decode them.
## Decoding Infrared Signals from Your Remote
  Since each string is essentially a “code” and we only need a few of those to make a basic robot go forward, reverse, left, and right. Pick 4 buttons on your remote to decode and let's start with those. To decode a signal, we just pick a button on the remote (ie. Volume Up) and push it several times to make sure the strings that you read on your Serial monitor are consistent (meaning it looks the same each time), then write it down. If you get a stray value here and there, don't worry – you will learn that infrared control is not the most reliable form of data transmission, but it will be perfect for our project. Then repeat this process for the rest of the buttons you plan on decoding, making sure to record the button you pushed to get the code you recorded.
  You should end up with a set of strings corresponding to the functions you would like on your robot. In chart 1.1 there are four signals from my infrared remote, each with 20 boolean values in a row. S1-S4 on the left side of the chart show the 4 different signals used, while the top row of numbers show the index number of each bit in the string:

Chart 1.1 – Plotting the values from each string onto a chart with the index values above.
Infrared Remote Signal Decode Chart
	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19

S1	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	0	0	0	0
S2	0	0	0	0	0	0	1	0	0	1	0	0	0	0	0	0	0	0	0	0
S3	0	0	0	0	0	0	1	0	0	1	1	0	0	0	0	0	0	0	0	0
S4	0	0	0	0	0	0	1	0	1	0	0	0	0	0	0	0	0	0	0	0

  As you can see from the chart, the only bits that changed between each button press were in index positions 8, 9, and 10, where each set of bits is different between the four codes received. The key to decoding a signal is being able to ignore the similarities between each code and pick out what makes them different – the differences are what we will test for in our code. That being said, you can see that I changed the color of all numbers on the chart that were not unique and made the unique values bold.
  The signals in the chart above could be simplified and defined in your Arduino code as shown below. Each time you read a new signal from the IR remote, you can check the substring(8,11) to see if is equal to any of the the signals that you have recorded, if so you can then carry out a specific action.
Signal_1 = “000”
Signal_2 = “010”
Signal_3 = “011”
Signal_4 = “100”

  At this point, it should be fairly easy to see how you could use the codes from each button to take control of your robot. Using a few “if/else” statements, we can quickly throw together a test to separate each code into a different robot action.

Code example 1.7 – Comparing decoded substrings with a test string

  String IRstring = "00000010010000000000"; // index positions 8, 9, and 10 are underlined

  if (IRstring.substring(8,11) == "000"){
    // Go Forward!
    // False
  }
  else if (IRstring.substring(8,11) == "010"){
    // Go Reverse!
    // This statement is TRUE
  }
  else if (IRstring.substring(8,11) == "011"){
    // Go Left!
    // False
  }
  else if (IRstring.substring(8,11) == "100"){
    // Go Right!
    // False
  }

  Now you should be able to decode as many other buttons as you like, keeping in mind that if you introduce other buttons, you will need to compare them against your original codes to confirm that no conflicts were introduced with the indexes that you are testing against. It is possible that if you add more codes to your chart, you may notice another index that was not previously an active bit.

## Infrared Helicopter Remote

  Using a TV remote is neat when you are testing, but ultimately it is nice to have real-time control of your robot. A TV remote will only send out signals when you press a button, causing the robot to have jerky movements and be difficult to control. Some infrared remote controls (specifically toy Infrared helicopter remotes) send out a constant stream of pulse signals that will keep our robot moving, these are much easier to use and can be used without harming your toy helicopter. If you don't have a toy helicopter, you might still be able to find one from a friend with a broken helicopter or from the thrift-store for a few dollars. If you cannot locate one, you can still use the standard TV remote method to control your robot.
Most infrared helicopter remotes have simple functions like throttle speed, turning, one or two buttons, and a mode selector switch to allow multiple helicopters to be operated in the same vicinity without interference. We can fairly easily decode these signals to determine the intended function. Let's start with the mode switch.
### Decoding Mode (optional)
The typical IR helicopter remote has a switch for modes A, B, and C. To accomplish this, the selector switch shifts all of the bits to the down one index position from A to B, then another position from B to C. You might have noticed that the index position 6 in charts 1.1, 1.2, and 1.3 always has a value of “1”. This is because mode A sets index position as the start bit to signal what mode it is in. We don't actually need to check for this value as the code will work in any of the modes. But if you care to operate multiple robots at the same time, we could add a conditional statement for this case... we are going to leave that feature for another day, though here is the chart depicting the values for each mode:

Table 1.2 – chart of the speed values I recorded from my IR helicopter remote
0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19

MA	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	0	0	0	0
MB	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0	0
MC	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	0	0	0	0	0

### Decoding Speed
  The first step to decoding these signals is to upload the code and open your Serial monitor. Now turn on your IR remote and move the throttle stick – this should prompt some signals to be read by your Arduino and appear on your serial monitor window. The first thing I would do is count the number of digits that consistently appear in each string (I observed 20 digits per string). Here is a table of the values I observed – the top row is the index of each string character and the S1 – S14 represents the 14 different speed signals I recorded:

Table 1.3 – chart of the speed values I recorded from my IR helicopter remote
	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19
S1	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	0	0	0	0
S2	0	0	0	0	0	0	1	0	0	1	0	0	0	0	0	0	0	0	0	0
S3	0	0	0	0	0	0	1	0	0	1	1	0	0	0	0	0	0	0	0	0
S4	0	0	0	0	0	0	1	0	1	0	0	0	0	0	0	0	0	0	0	0
S5	0	0	0	0	0	0	1	0	1	0	1	0	0	0	0	0	0	0	0	0
S6	0	0	0	0	0	0	1	0	1	1	0	0	0	0	0	0	0	0	0	0
S7	0	0	0	0	0	0	1	0	1	1	1	0	0	0	0	0	0	0	0	0
S8	0	0	0	0	0	0	1	1	0	0	0	0	0	0	0	0	0	0	0	0
S9	0	0	0	0	0	0	1	1	0	0	1	0	0	0	0	0	0	0	0	0
S10	0	0	0	0	0	0	1	1	0	1	0	0	0	0	0	0	0	0	0	0
S11	0	0	0	0	0	0	1	1	0	1	1	0	0	0	0	0	0	0	0	0
S12	0	0	0	0	0	0	1	1	1	0	0	0	0	0	0	0	0	0	0	0
S13	0	0	0	0	0	0	1	1	1	0	1	0	0	0	0	0	0	0	0	0
S14	0	0	0	0	0	0	1	1	1	1	0	0	0	0	0	0	0	0	0	0

  Next, you should check to see what digits change when you move your throttle stick. I noticed that the digits in index positions 7, 8, 9, and 10 changed as I moved the throttle to 100%. So I opened up a Spreadsheet (Libre Office is open-source) and recorded each unique value as I moved the throttle control. When I was finished recording, I recognized 14 different speed steps that had unique codes, so I recorded these 4 digit values as variables in my Arduino sketch (speed1 through speed14). If you record different values, you can change the variables that I made to match your own values. You shouldn't have to change any functions in the code, just the String variables at the top of the sketch as shown in code example 1.8:

Code example 1.8 – Setting some String objects with our recorded substrings to test against for speed.
String speed1 = "0000";
String speed2 = "0010";
String speed3 = "0011";
String speed4 = "0100";
String speed5 = "0101";
String speed6 = "0110";
String speed7 = "0111";
String speed8 = "1000";
String speed9 = "1001";
String speed10 = "1010";
String speed11 = "1011";
String speed12 = "1100";
String speed13 = "1101";
String speed14 = "1110";

  The decode_speed() function is in place to contain some “if” statements to determine what speed value the infrared controller is sending across. Since I recorded 14 different speed step values, I wanted to break up each step into equal speed increases as to smooth out the acceleration and turning. The Arduino PWM value ranges from 0 to 255, so we need to break this range up into 14 somewhat equal parts. We could have mapped the value from 1-14, to 0-255 – but I decided that it was easier to read by listing each speed increase out in the code as shown in code example 1.9.

Code example 1.9 – Decoding the speed values using some conditional statements (if/else).

void decode_speed(){
  // check values of indexes 7 through 10 of IRstring to see if they are equal to any of the recorded speed values (speed1-14)
  // Arduino PWM max speed value is 255, I measured 14 speed values (steps) from the IR sensor.
  // 255/14 = 18.2, so I started at PWM 0 with speed1 and incremented by 20 (rounded up from 18.2) for each speed step until reaching PWM 255 with speed14.
  if (IRstring.substring(7,11) == speed1){speed_val = 0;}
  else if (IRstring.substring(7,11) == speed2){speed_val = 20;}
  else if (IRstring.substring(7,11) == speed3){speed_val = 40;}
  else if (IRstring.substring(7,11) == speed4){speed_val = 60;}
  else if (IRstring.substring(7,11) == speed5){speed_val = 80;}
  else if (IRstring.substring(7,11) == speed6){speed_val = 100;}
  else if (IRstring.substring(7,11) == speed7){speed_val = 120;}
  else if (IRstring.substring(7,11) == speed8){speed_val = 140;}
  else if (IRstring.substring(7,11) == speed9){speed_val = 160;}
  else if (IRstring.substring(7,11) == speed10){speed_val = 180;}
  else if (IRstring.substring(7,11) == speed11){speed_val = 200;}
  else if (IRstring.substring(7,11) == speed12){speed_val = 220;}
  else if (IRstring.substring(7,11) == speed13){speed_val = 240;}
  else if (IRstring.substring(7,11) == speed14){speed_val = 255;}
  else {speed_val = 0;} // if the string cannot match any of the recorded values, set the speed value to 0 PWM (stop).

  // set both m1_val (motor 1) and m2_val (motor 2) equal to the speed_val we just set above
  m1_val = speed_val;
  m2_val = speed_val;
}

As you can see, this code is very straightforward – if the 4 digits of the string that we care about (indexes 7-10) for the speed decoding match any of the recorded values from our chart above, set the speed value accordingly (between 0 and 255). Otherwise, if no signal is received, turn the motors off. After calculating the initial value forhttp://arduino.cc/en/Reference/StringObject each motor based only on the speed_val, we must now factor in the turning bias if one exists.
### Decoding Turn
  Decoding the turn signal is much easier than the speed, because I only observed 6 steps of resolution total for both left and right. This means that there are only 3 steps to the left and 3 steps to the right. As it turns out, this is more than enough resolution to precisely steer our robot – remember that we also have 14 steps of speed resolution to combine with each of the 3 steps of steering resolution... this provides more control than you might guess. I noticed when observing the Serial monitor strings produced when I moved the steering control stick only, that the only bits that moved were in index positions 15, 16, and 17. These are my recorded unique steering values:

Chart 1.4 – chart of the turn values I recorded from my IR helicopter remote
	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19
R1	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	0	1	0	0
R2	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	1	0	0	0
R3	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	0	1	1	0	0
L3	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	1	0	1	0	0
L2	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	1	1	0	0	0
L1	0	0	0	0	0	0	1	0	0	0	0	0	0	0	0	1	1	1	0	0

  Again, the active values for the steering function are contained in only 3 bits, making this decoding easier than with the 4-bit speed code. As you can see, we set these unique codes as string objects in our Arduino code and use them later to compare against the IRstring. Since we only have 6 turning codes, we will only have 6 “if” statements to check the turn values.

Code example 1.10 – Setting some String objects with our recorded substrings to test against for turn.

// turning codes are contained in indexes 15, 16, & 17
String right1 = "001";
String right2 = "010";
String right3 = "011";
String left3 = "101";
String left2 = "110";
String left1 = "111";

  As you can see, there are far fewer codes used for steering than for the speed. As with the speed values, if your steering values have different boolean values, you can change them in the String variable declarations above. After declaring the unique codes, we can simply use the decode_turn() function to check the index positions 15, 16, and 17 to see if they match the recorded string variables listed. If there is any match, a corresponding turn bias is applied to the m1_val and m2_val variables to make one slower than the other. On a tank steering robot, slowing down either motor will make the robot turn in that direction – with this in mind, I chose some arbitrary biases for each of the 3 turning stages. The first should be subtle, so I left one motor alone and divided the other in half to make the robot turn. The second step should be more noticeable but still controllable, so I more drastically set the one motor to 0 and other to double its value – this makes a much more aggressive turn rate. Lastly, the third stage is used to turn in place. Also called a “zero-turn”, this occurs when one motor spins forward and the other motor spins in reverse, effectively spinning in place – the speed value still determines how fast each motor spins.

Code example 1.11 – Setting some String objects with our recorded substrings to test against for turn.

void decode_turn(){
  // check for a turn code (there were 6 unique codes on my remote)
  // 3 steps in each direction
  if (IRstring.substring(15,18) == left1){
    // turn left slightly (left1)
    m1_val = speed_val / 2;
    m2_val = speed_val;
  }
  else if (IRstring.substring(15,18) == left2){
    // turn left moderately (left2)
    m1_val = 0;
    m2_val = speed_val * 2;
  }
  else if (IRstring.substring(15,18) == left3){
    // turn left extremely (left3)
    m1_val = -speed_val;
    m2_val = speed_val;
  }
  else if (IRstring.substring(15,18) == right1){
    // turn right slightly (right1)
    m2_val = speed_val / 2;
    m1_val = speed_val;
  }
  else if (IRstring.substring(15,18) == right2){
    // turn right moderately (right2)
    m2_val = 0;
    m1_val = speed_val * 2;
  }
  else if (IRstring.substring(15,18) == right3){
    // turn right extremely (right3)
    m2_val = -speed_val;
    m1_val = speed_val;
  }
  else {
    // otherwise, do nothing to the speed values
  }
}

  You might have noticed how some of the speed values are changed to negative. This is not how the values are written to the motor-controller (as a negative number would not work for PWM), but instead how we will determine if a motor should be going in reverse. Later in the sketch there is a failsafe that re-converts the signal back to positive before being written to the motor-controller. Now we can check the button (if applicable) to use for reversing our robot.

### Decode Button
Most IR helicopter remotes have a speed control stick that only allows forward motion and defaults to 0% instead of center positioned at 50% for forward and reverse control using one stick. This is because toy helicopter blades do not reverse direction during flight, but instead only go forward. If we would like to implement a “reverse” feature, it will need a separate channel on our remote – luckily most IR helicopter remotes have a set of buttons used to “trim” the helicopter rotation during flight. Since we will (hopefully) not be spinning uncontrollably on our robot, we can use these buttons for something else, like reversing.
  Recall that to reverse the robot in our sketch, you must simply change either motor value (m1_val or m2_val) to be negative and it will then reverse its direction. This works quite well in practice and still listens to the speed_val to determine the overall speed in reverse. Even when turning and one motor value is already negative, pressing the button will reverse the polarity of both motors, causing the direct opposite turn effect that you experience when going forward. Below is a chart of the bit indexes that changed when I pressed the button on my remote.

Chart 1.5 – chart of the button values I recorded from my IR helicopter remote
	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19
R1	0	0	0	0	0	0	1	0	0	0	0	1	1	1	1	0	0	0	0	0
R2	0	0	0	0	0	0	1	0	0	0	0	0	0	0	1	0	0	0	0	0

  The button changes four different bits from 11 to 14, though there were really only two of them (index 13 and 14) are required to determine the position of both buttons.

Code example 1.12 – Setting some String objects with our recorded substrings to test against for buttons.
// button codes are contained in indexes 11, 12, and 13
String button_left = "1111";
String button_right = "0001";

void decode_button(){
  // check button to see if being pushed
  // if so, we will use this for reverse by making the speed value negative
  if (IRstring.substring(11,15) == button_left){
    // left button was pushed.. we are not currently checking for the right button
    m1_val = -m1_val; // set the current speed value for each motor negative
    m2_val = -m2_val; // setting the value negative, makes that motor go in reverse
  }
}

Limit Signal

  The signal limiting function is used to make sure no erroneous values are sent to the motor-controller. Since the Arduino's possible PWM value ranges from 0 to 255, we don't want to write any values above 255 because the Arduino will then throw an electronic temper tantrum and start writing random values to the motor-controller, which usually makes the robot start acting sporadic. This isn't the end of the world, but it can heat up your motor controller and is annoying, so this simple function takes care of it.

Code example 1.13 – The limit_signal() function used to keep our motor values in check
void limit_signal(){
  // this is just a function to check each motor value and make sure neither exceeds +/-255
  // if either value does, set it to the max of +/-255... we don't want any sporadic values sent to the motor-controller
  if (m1_val > 255){ m1_val = 255; }
  else if (m1_val < -255){ m1_val = -255; }

  if (m2_val > 255){ m2_val = 255; }
  else if (m2_val < -255){ m2_val = -255; }
}

  Remember that to reverse a motor using this code, we simply set the motor value (m1_val or m2_val) to be negative - we will convert those values back to positive, but not yet. For now, we will just make sure that if m1_val is above 255 or below -255, then we should just go ahead and cap the value at its max (+/-255). Then obviously do the same for m2_val. Now it is time to convert these values into forward or reverse speed values and write those values to the motors.

Write Motors

 To write values to the motors, we will use the motor functions discussed in the MakeBlock chapter. Here will simply call those functions (m1_forward(), m2_reverse(), etc..) and pass in the PWM speed value for that motor, either m1_val or m2_val. Deciding what direction to go is likewise easy to determine - positive values go forward and negative values go reverse. If the value is 0, just stop that motor.
  We will leave positive values alone and send them to the forward motor commands. Remember that we cannot actually write a negative value to the motors, so we will reverse the polarity of negative values by simply adding a negative sign in front of the variable, thereby sending a positive value to the reverse motor commands. Again, stop each motor separately using the motor stop commands. The below function uses some “if” statements to check the polarity of the value and then accordingly write either m1_forward(m1_val), m1_reverse(-m1_val), or m1_stop() to set the direction (likewise for m2).

Code example 1.13 – The write_motors() function used to take the calculated speed value for each motor and send it to the motor-controller.
void write_motors(){
  // check direction of m1_val and write appropriately
  if (m1_val > 0){
    // if m1_val is above 0, we are going forward, using m1_val to set the PWM duty-cycle (motor speed)
    m1_forward(m1_val);
  }
  else if (m1_val < 0){
    // if m1_val is below 0, go reverse using -m1_val (which will now be a positive number) to set the PWM duty-cycle.
    m1_reverse(-m1_val);
  }
  else {
    m1_stop(); // otherwise, stop this motor
  }
  // check direction of m2_val and write appropriately
  if (m2_val > 0){
    // if m2_val is above 0, we are going forward using m1_val to set the PWM duty-cycle (motor speed)
    m2_forward(m2_val);
  }
  else if (m2_val < 0){
    // if m2_val is below 0, go reverse using -m1_val (which will now be a positive number) to set the PWM duty-cycle.
    m2_reverse(-m2_val);
  }
  else {
    m2_stop(); // otherwise, stop this motor
  }
}

Now that we have discussed each individual function in the sketch, we will go through the main loop function to show what is happening.

Putting it all together: the loop() function

  The main loop function is the core of what we are doing in this sketch – all of the functions that we have discussed so far are called from the main loop function. The very first thing we will do is call the pulse() function which will call the pulseIn() command to read the pin we connected the IR receiver to (pin 6 for me). If there is a pulse present on this pin, a variable called pulse_val will be set equal to the length of time that the pulse was HIGH from the IR receiver, in microseconds.
  The next step after reading the pulse_pin, is to check the new value to see if it contains a valid pulse (greater than 0 microseconds). If so, we will then assume that a new set of pulses is being received and we should start to build the String object. Set the “reading” variable equal to true to indicate that we have just read a valid pulse (this is a flag that is useful in the next cycle).
  Now it is time to booleanize() the pulse value we just received – remember that this just checks the length and converts it into either a 1 or 0 to be appended to the string. Next we will add the new booleanized pulse_val into the end of the string called “IRstring”, using the += operator that simply says a += b is the same as a = a + b.
  Finally, we will set the loop_counter variable equal to 0, to signify that it has been 0 loop cycles since we last read a valid pulse signal (we just read one). This counter variable is useful when we stop reading pulses, so we know how long it has been since the last valid pulse. If it has only been 3 or 4 loop cycles since the last signal (a fraction of a second), we should just let the robot keep doing what it was doing when it last received a good signal... though if it has been 100 or so cycles since receiving a good signal (about 1 second or so), we should probably stop the robot to keep it from hitting something. Skipping a few bad signals keeps the robot from being jerky and sporadic every time a signal is distorted or fails to reach the sensor, while also not giving it enough time to get out of control.
  As long as we are receiving a train of pulse signals, this process will repeat 20 or so times until we reach the end of the pulses for that signal. Skip down below the code to see what happens when we stop receiving pulses.
Code example 1.14 – The main loop() function.
void loop() {
  // get a pulse reading from the IR sensor
  pulse();
  // now check to see if it is a valide pulse was read (any pulse greater than 0 microseconds)
  if (pulse_val > 0){
    reading = true; // if so, assert that we are reading a pulse (so we will later know when the pulses stop)
    booleanize(); // convert each current pulse into a boolean 0 or 1
    IRstring += pulse_val; // append each new value to a string data object instead of an array.
    loop_counter = 0; // since we just read a pulse, reset the pulse counter to 0.
  }
  // else if the pulse is not greater than 0...
  else {
    // if this is the first non-pulse loop cycle after a set of pulses, go ahead and close out the string
    if (reading == true){
      // OK, we have the end of a signal. Now let's check to make sure the resulting IRstring is long enough
      if (IRstring.length() >= string_length){
        // if the string we just got is the appropriate length, let's get moving!
        decode_speed(); // check speed value
        decode_turn(); // check for turn
        decode_button(); // check button for reverse signal
        limit_signal(); // check and limit the signal so no bad value is written to the H-bridge
        write_motors(); // finally, write the values to the motors
      }
      Serial.println(IRstring); // Now print the full String to the Serial monitor
      IRstring = ""; // and set the string object to be empty "", so we can start over
    }
    reading = false; // since we are no longer reading a pulse anymore, set the reading value to false
    loop_counter++; // increment the loop counter by adding 1 to it
    // check to see if the loop count has reached 100 cycles without receiving a pulse signal
    if (loop_counter > 100){
      // at this point, it has been 100 loop cycles (a second or so) without receiving an IR signal
      m1_stop(); // so we need to stop both motors
      m2_stop(); // to keep the robot from driving off into the sunset without us
      loop_counter = 0; // also, since we have stopped the robot, we can reset the loop counter
    }
  }
}

  Alright, so we are in the middle of the loop just after the first “if” statement, and the pulse value has been determined to be invalid (there is no pulse). We will now need to check and see if the last loop cycle detected a pulse, if so that means this is the first loop cycle after a set of pulses and we need to close this string so it can be passed through our speed, turn, and button tests. We do this by checking the “reading” variable to see if it is true or false. If true, we should proceed to close the string, evaluate it, then write the resulting values to the motors.
  Before we close the string and writing the values to the motors, we should first check to make sure the string that we just received is not missing any bits. I counted the number of characters in each string (disregarding the occasional shorty), and recorded this number to the “string_length” variable – my string length is 20 characters. If the current string is 20 characters in length, we can go ahead and evaluate it.
  This is where we call the functions that we discussed earlier: decode_speed(), decode_turn(), decode_button(), limit_signal(), and write_motors(). We will not go over these again, but you can revisit the explanation for each earlier in the chapter. Once we have written the newly decoded values to the motors, we should print the string to the serial monitor and empty it (set it equal to an empty string “”) so we can start building the next string in its place.
  For the last part of the loop we will be dealing with the condition when we go through the loop and have neither read a pulse in the last loop cycle nor are we reading one currently. We are setting the “reading” variable to false each time we pass through this condition because we are not reading any pulses. Also we are adding 1 to the loop_counter variable to signify another loop cycle past with no pulse – at this point we are considering stopping the robot. Before we cut the power, let the loop_counter variable increment up to 100 loop cycles with no pulse before we go ahead and pull the plug on the motors and wait for another valid pulse. After 100 cycles with no pulse, let the motors stop – it safe to say, we are not getting a signal from the remote any more.... but be patient and wait for the next pulse.

Testing and Debugging

  That's it! You should be driving your infrared controlled robot around with a helicopter remote – if this is your first act of hackery, congratulations!
  If your robot is not working on the first try, you might need to double check some things:

- Let's first rule out your robot frame and motor-controller setup by referring back to the MakeBlock chapter for how to set up your robot frame, motor-controller connections, and get the appropriate direction commands working with the Arduino alone before trying to troubleshoot with the IR sensor.
- Did you check the serial monitor to make sure your Arduino is reading a valid string of characters (0 and 1 bits)? If not, connect your Arduino to your computer via USB cable and open the Arduino IDE, then the Serial monitor and make sure the baud rate is set to 9600bps.
- If you do not see any string come across the serial monitor when you activate the remote, make sure the IR receiver module is connected correctly: left pin: Arduino D6, center pin: Ground, right pin: +5v.
- Next make sure your IR remote is sending a signal – you can check by looking through a digital camera (your camera phone will work) at the IR LED on the end of the remote and moving the throttle control stick to see if the LED lights up purple. You wont be able to see it with your naked eye – the camera acts as a light filter. If you do not see any values still, it is possible that you have an unsupported remote control. Try another IR remote to make sure – if you get values from the second remote, you will have your answer.
- If you are getting strings to come across on the serial monitor and they are 20 characters in length but you are not getting movement, make sure the correct index positions are changing when you move the respective controls (speed, turn, button). Refer to the decoding charts for the values I used. If you have different values, you will need to modify the speed, turn and button variables to reflect your values – the rest of the code should work the same.